28 October 2016
Cryptographic Randomness on a CC2538:
A Case Study
Yan YAN, Elisabeth OSWALD, Theo TRYFONAS

---
CC2538
(http://www.ti.com/product/CC2538)
- ARM® Cortex®-M3
- 512KB, 256KB or 128KB Programmable Flash
- 2.4-GHz IEEE 802.15.4 Compliant RF
- Security Hardware Acceleration
- Low Power
- Zigbee/6LoWPAN Support

---
Random Number Generators (RNGs)
True RNG (TRNG)
  - Samples entropy in physical source
Pseudo RNG (PRNG)
  - Seeded by TRNG
  - Efficient
Cryptographic Usage:
  - Key Generation, etc

---
Sad Stories...

---
CC2538 PRNG
- Coding Issues in Contiki driver
- 16 bit LFSR (CRC16) as PRNG
2^16 = 65536
Far NOT ENOUGH for cryptographic security!

---
e.g.: Broken ECDHE/ECDSA in DTLS (tinydtls)
Build Key Pair lookup table: 65536 entries
Revert r_A from Q_A and r_B from Q_B.
Compute Q_{AB}.
Revert k from r.
Extract d given (s,k,e,r).

---
CC2538 TRNG: Sampling RF noise
- Passed NIST test tool(*), but...
- Potentially tamperable.
(*)http://csrc.nist.gov/groups/ST/toolkit/rng/documentation_software.html

---
Hints of Circuit Design:
CC2520 Manual
CC2420 Manual

---
- Fixed ADC input – fixed ADC output (fixed LSB)
  - Use constant signal (i.e. carrier wave)
  - Challenge: Noises affect LSB
AGC Circuit
  - Solution: Saturation (strong signal)
      - Noises became negligible.

---
Result

---
Conclusion
- Really Not Good RNG:
  - Low entropy PRNG
      - Not recommended for any security usage.
  - Tamperable Entropy Source
      - Needs to be physically protected.
- Use Dedicated RNG:
  - Latest CC Series: