5 December 2016
Cryptographic Randomness on a CC2538:
A Case Study
Yan YAN, Elisabeth OSWALD, Theo TRYFONAS

---
CC2538
(http://www.ti.com/product/CC2538)
- ARM® Cortex®-M3
- 512KB, 256KB or 128KB Programmable Flash
- 2.4-GHz IEEE 802.15.4 Compliant RF
- Low Power Consumption
- Contiki OS Support
- Cryptographic Hardware Acceleration

---
Random Number Generators (RNGs)
True RNG (TRNG)
  - Samples entropy in physical source
Pseudo RNG (PRNG)
  - Seeded by TRNG
  - Efficient
Cryptographic Usage:
  - Key Generation, etc

---
Example: RNG in EC Key Generation
Example: tinydtls implementation
- Random value as sk.
- pk = [sk]*G

---
Sad Stories...

---
CC2538 PRNG
16 bit LFSR (CRC16) as PRNG
2^16 = 65536
NOT ENOUGH for cryptographic security!

---
e.g.: Broken ECDHE/ECDSA in DTLS
Build Key Pair lookup table: 65536 entries
Revert r_A from Q_A and r_B from Q_B.
Compute Q_{AB}.
Revert k from r.
Extract d given (s,k,e,r).

---
CC2538 TRNG: Sampling RF noise
Potentially tamperable.
(*)http://csrc.nist.gov/groups/ST/toolkit/rng/documentation_software.html

---
Hints of Circuit Design:
CC2520 Manual
LSB of I/Q ADC as RNG.
CC2430 Manual

---
- Fixed ADC input – fixed ADC output (fixed LSB)
  - Use constant signal (i.e. carrier wave)
  - Challenge: Noises affect LSB
AGC Circuit
  - Solution: Saturation (strong signal)
      - Noises became negligible.

---
Result (on 128 bit seed)
Abnormal continuous 0s in seeds.
Frequency of 0
Continuous 0 bits

---
Conclusion
- Really Not Good RNG:
  - PRNG: Low entropy.
      - Not recommended for any security usage.
  - TRNG: Entropy source can be tampered.
      - Needs to be physically protected.
- Use Dedicated RNG:
  - Latest CC Series: CC2650, etc.